High Performance Non-blocking Switch Design in 3D Die-Stacking Technology
Dean L. Lewis, Sudhakar Yalamanchili,
Hsien-Hsin S. Lee
IEEE Computer Society Annual Symposium on VLSI
Tampa, Fl, 2009
http://arch.ece.gatech.edu/mars.html

---
3D Integration
Multiple layers of silicon

---
3D Integration
- Multiple layers of silicon
- Interconnected with TSVs
  - Etched through thinned wafers

---
3D Integration
- Multiple layers of silicon
- Interconnected with TSVs
  - Etched through thinned wafers
- Several integration options
  - Technology
    - Different processing technologies are tightly integrated

---
3D Integration
- Multiple layers of silicon
- Interconnected with TSVs
  - Etched through thinned wafers
- Several integration options
  - Technology
    - Different processing technologies are tightly integrated
  - Architecture
    - Blocks split across layers
ALU 0
ALU 1
ALU 2
ALU 3

---
3D Integration
- Multiple layers of silicon
- Interconnected with TSVs
  - Etched through thinned wafers
- Several integration options
  - Technology
    - Different processing technologies are tightly integrated
  - Architecture
    - Blocks split across layers
  - Circuit
    - Transistors split across layers

---
Switch Design
INPUTS
OUTPUTS

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
- Weakly non-blocking
  - Any free input/output pair can be connected
  - Existing connections may need to be rearranged
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
- Weakly non-blocking
  - Any free input/output pair can be connected
  - Existing connections may need to be rearranged
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
- Weakly non-blocking
  - Any free input/output pair can be connected
  - Existing connections may need to be rearranged
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
- Weakly non-blocking
  - Any free input/output pair can be connected
  - Existing connections may need to be rearranged
- Blocking
  - Making a new connection may disconnect an existing connection
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
- Weakly non-blocking
  - Any free input/output pair can be connected
  - Existing connections may need to be rearranged
- Blocking
  - Making a new connection may disconnect an existing connection
Connect(3,2)

---
Switch Design
- Strictly non-blocking
  - Any free input/output pair can be connected
  - No effect on existing connections
- Weakly non-blocking
  - Any free input/output pair can be connected
  - Existing connections may need to be rearranged
- Blocking
  - Making a new connection may disconnect an existing connection
Connect(3,2)

---
Crossbar
- Strictly Non-blocking
- Lots of switch points
- Little wiring

---
Crossbar
- Strictly Non-blocking
- Lots of switch points
- Little wiring
- Very long critical path
Connect(15,15)

---
Row-Split 3D Crossbar
- Cannot target wiring directly
  - Too short and direct
- Instead, change critical path using 3D design
- Split rows in half, placing each half on a different layer
- Add multiplexers to bypass unused half
- Critical path wirelength is reduced by 25%

---
Row-Split 3D Crossbar
- Cannot target wiring directly
  - Too short and direct
- Instead, change critical path using 3D design
- Split rows in half, placing each half on a different layer
- Add multiplexers to bypass unused half
Connect(15,15)

---
Column-Split 3D Crossbar
Complimentary to row-split design

---
Column-Split 3D Crossbar
Complimentary to row-split design
Connect(15,15)

---
Column-Split 3D Crossbar
- Complimentary to row-split design
- Row-split and column-split designs can be applied simultaneously in a four-layer stack
  - 50% reduction in critical path wirelength
Connect(15,15)

---
Crossbar – System View
- Crossbars are great at small sizes
- This makes them good for a NoC design
  - Individual components (processors, routers, caches) are 3D
  - NoC architecture is planar (shown)
  - Of course, both components and NoC could be 3D
P2
P3
P0
P1

---
Crossbar – System View
- Crossbars are great at small sizes
- This makes them good for a NoC design
  - Individual components (processors, routers, caches) are 3D
  - NoC architecture is planar (shown)
  - Of course, both components and NoC could be 3D
P2
P3
P0
P1

---
MIN
- Multistage interconnect network
- Weakly non-blocking
- Less hardware but more complex wiring than crossbars
- Usually more appropriate for larger switches
- Example system: many-input router chip
Interconnect Stage
Interconnect Stage
Interconnect Stage
Interconnect Stage
Interconnect Stage
Interconnect Stage

---
Perfect Shuffle
- Interconnect pattern – deck of cards perfectly shuffled
- Lots of overlapping wiring, so lots of wiring tracks

---
Perfect Shuffle
- Interconnect pattern – deck of cards perfectly shuffled
- Lots of overlapping wiring, so lots of wiring tracts
- Two long hops on critical path: (3,7) and (4,0)

---
Perfect Shuffle – Wiring
Pattern in the overlaps that 3D can target to relieve congestion

---
Perfect Shuffle – Wiring
- Pattern in the overlaps that 3D can target to relieve congestion
- Nodes 0 and 4 both connect to 0 and 1 in the next stage

---
Perfect Shuffle – Wiring
- Pattern in the overlaps that 3D can target to relieve congestion
- Nodes 0 and 4 both connect to 0 and 1 in the next stage
- Similarly, nodes 3 and 7 share 6 and 7

---
3D Perfect Shuffle
- Split MIN into bottom half and top half
- Place top half over bottom half

---
3D Perfect Shuffle
- Split MIN into bottom half and top half
- Place top half over bottom half
- Those old longest paths are now much shorter

---
3D Perfect Shuffle
- Split MIN into bottom half and top half
- Place top half over bottom half
- Those old longest paths are now much shorter
- Consequently, critical path is reduced

---
Butterfly Shuffle
- Interconnect pattern – wiring destination doubles at each stage
- Lots of overlapping wires in the outer stages

---
Butterfly Shuffle
- Interconnect pattern – wiring destination doubles at each stage
- Lots of overlapping wires in the outer stages

---
Butterfly Shuffle
- Interconnect pattern – wiring destination doubles at each stage
- Lots of overlapping wires in the outer stages
- These wires do not share switch resources

---
Butterfly Shuffle
- Interconnect pattern – wiring destination doubles at each stage
- Lots of overlapping wires in the outer stages
- These wires do not share switch resources

---
3D Butterfly Shuffle
- Use a “bit-split” partition
- This removes half of overlapping wires from each outer stage

---
3D Butterfly Shuffle
- Use a “bit-split” partition
- This removes half of overlapping wires from each outer stage
- Now many fewer wiring tracts required per stage

---
3D Butterfly Shuffle
- Use a “bit-split” partition
- This removes half of overlapping wires from each outer stage
- Now many fewer wiring tracts required per stage
- Critical path is significantly reduced

---
Experimental Setup
- Switch cell
  - 130nm technology
- TSV
  - Tezzaron 3D process
  - 10um x 1.7um x 1.7um
- HSPICE simulation
  - Lvl49 130nm transistor
  - Stick diagrams for wiring stages
  - Intel 130nm wire parasitics

---
Results
1.02
1.01
0.93
0.92
0.91
0.90
0.88
0.85
0.80
0.76
0.76
0.74

---
Conclusion
- Switches are a key component of networks both large and small
- 3D integration can be used to effectively improve switch performance
- 3D circuit design effectively targets and reduces long critical paths
- Generally, 3D integration reduces area, delay, and energy simultaneously
- These reductions are significant
  - 8% - 26%
- 3D will be a powerful design optimization technology in near-future products

---
Thank you!
http://arch.ece.gatech.edu/mars.html