## Slide 1: Heterogeneous Die Stacking of SRAM Row Cache and 3-D DRAM: An Empirical Design Evaluation
Dong Hyuk Woo
Nak Hee Seong
Hsien-Hsin S. Lee
The 54th IEEE International Midwest Symposium on Circuits and Systems
Electrical and Computer Engineering
Georgia Tech
Intel Labs

## Slide 2: Modern DRAM Design Challenges
Scaling challenge
  Less capacity
  Higher leakage
Increasing manufacturing cost
Energy efficiency pressure
  Smart phone / tablet
  Cloud / Exa-scale computing

## Slide 3: Future Solutions
Homogeneous stacking [Kang et al., JSSC 2010]
Increasing density without scaling the device
Heterogeneous stacking [Kawano et al., IEDM 2006]
Dedicating a logic layer for I/O circuit
Better performance, lower energy consumption

## Slide 4: New Opportunity for Processor Architects
SPACE
AVAILABLE
(404) 894-9483

## Slide 5: SRAM Row Cache?

## Slide 6: An Optimized 3D-Stacked Memory Architecture by Exploiting Excessive, High-Density TSV Bandwidth by D. H. Woo, N. H. Seong, D. L. Lewis and H.-H. S. Lee in IEEE International Symposium on High-Performance Computer Architecture (HPCA-16), 2010.
Motivation

## Slide 7: Row Buffer Conflicts in a Multi-core
Conventional
3D DRAM
Row Buffer
Hit rate ~ 50%
One entry / bank
One cache line
0x0000 0000
0x0000 0040
0x1000 0000
0x1000 0040
0x0000 0080
0x0000 00c0
Address Stream
3 row misses
3 row hits

## Slide 8: Eliminating Redundant Array Lookup
Heterogeneous
SRAM row cache
+ 3D DRAM
0x0000 0000
0x0000 0040
0x1000 0000
0x1000 0040
0x0000 0080
0x0000 00c0
One row cache line
Row cache Hits
Address Stream
Row Cache
2 row misses
4 cache hits

## Slide 9: SRAM Row Cache Stacking
High bandwidth, low energy communication through TSVs
Large set-associative SRAM row cache
Eliminating redundant DRAM look-ups
caused by conflict misses in row buffers

## Slide 10: Conventional DRAM Bank Structure
2-D transfer is still energy hungry!
Large area overhead of TSV
TSVs
One bank per die
Not drawn to scale

## Slide 11: Folded, Scalable DRAM Bank Structure
Short transfer of large data (a row)
Long transfer of small data (a cache line)
64x64TSVs
64x16TSVs
One half-row = 4Kb (64x64)

## Slide 12: Final Design: SRAM Row Cache + 3-D DRAM
One SRAM cache bank per DRAM bank

## Slide 13: Performance Results
Performance: Overall Speedup
Performance: Row Hit Rate

## Slide 14: Energy Results
Energy: Relative DRAM Lookup Energy

## Slide 15: Energy Breakdown
Chart: Relative Dynamic Energy
| DRAM (open row) | DRAM (closed row) | Hetero. (8-entry) | Hetero. (16-entry) | Hetero. (32-entry)
DRAM array lookup | 0.74537 | 1.2054 | 0.48244 | 0.33876 | 0.25775
SRAM | 0 | 0 | 0.21543 | 0.21532 | 0.21531
TSV | 0 | 0 | 0.041592 | 0.020404 | 0.01076
Refresh | 0.25395 | 0.31747 | 0.18716 | 0.18427 | 0.18245

## Slide 16: Conclusion
3-D stacking  new light for architects
SRAM row cache for 3-D DRAM
Folded DRAM bank design
Optimize 2-D Traffic
Significant energy savings

## Slide 17
That’s All, Folks!
Georgia Tech
ECE MARS Lab
http://arch.ece.gatech.edu

## Slide 18: BACKUP FOILS

## Slide 19: Simulation Results
Chart: Relative Value
| Speedup | Hit rate | DRAM array lookup energy
DRAM (open row) | 1 | 1 | 1
DRAM (closed row) | 0.89783 | 0 | 1.6172
Hetero. (8-entry) | 1.2812 | 1.6679 | 0.64724
Hetero. (16-entry) | 1.2921 | 1.7193 | 0.45449
Hetero. (32-entry) | 1.3002 | 1.7529 | 0.34581